## Slide 1: Codice TEE : Trasporti Energia Emissioni E. Negrenti - ENEA ANPA - 9 Novembre 2000

## Slide 2: MAIN CONTENTS
OBJECTIVES
VEHICLES KINEMATICS
MODELLED FACTORS
PARKING PROCESS SIMULATION
THE KINEMATICS CORRECTION

## Slide 3: 1) OBJECTIVES OF TEE MODEL
Link by link emission calculation
Flexible kinematics description
Modelling all factors affecting emissions
Separated analysis of parking process
Integration of the micro module (one link - one hour) in a year - network framework
Complete spatial-temporal flexibility

## Slide 4: 2. TEE MODEL KINEMATICS
VARIABLE KINEMATICS APPROACH
STRATEGIC COUPLING WITH ANY TRAFFIC MODEL OR DATA
AVERAGE SPEED OPTIONS
SIMPLIFIED CYCLE OPTIONS
DETAILED SPEED CYCLE OPTION
KINEMATICS CORRECTION FACTOR APPROACH (1998)

## Slide 5: 3. MODELLED FACTORS
ENGINE TEMPERATURE (LOCAL COLD VEHICLES FRACTION)
ROAD GRADIENT (SLOPE)
MAINTENANCE
AGE
ALTITUDE
DISTINCT PARKING FLOWS

## Slide 6: 4. PARKING PROCESS SIMULATION
PARKING AND INSERTING FLOWS FOR EACH LINK (‘P’ AND ‘I’ MODES)
CONCENTRATED AND DISTRIBUTED PARKING AREAS
SIMPLIFIED CYCLES FOR PARKING INLET AND OUTLET
P : DECELL., SEARCH, PARKING
I : WARM UP, EXIT, INSERTION

## Slide 7: 4.1 PARKING MODELLING
CONCENTRATED PARKINGS STATIC CHARACTERISATION
  PARKING INVENTORY (MAX. N. OF VEHICLES AND MACRO CATEGORIES ALLOWED)
  DISTANCE FROM LINK INLET TO PARKING PLACE - AND FROM PARKING TO LINK OUTLET
  LINKS OF INLET(S) AND OUTLET(S)
  COORDINATES OF PARKING AREA CENTRE FOR GIS REPRESENTATION

## Slide 8: 4.2 DISTRIBUTED PARKINGS STATIC CHARACTERISATION
DENSITY OF PARKING PLACES (VEH/KM) ALONG ROAD SIDES - DEFAULT CAN BE AROUND 200 V/KM
MACRO CATEGORIES ALLOWED TO PARK ALONG THE ROAD CONSIDERED (e.g. : Passenger Cars, 2 Wheelers, coaches)

## Slide 9: 4.3 Dynamic Description of Parking Areas (Concentrated or Distributed)
Occupation profile in 24h (from 0 to 1 of local inventory)
Input and Output flows (veh/hr) to-from linked vehicular flows
  from Concentrated parking : data from monitored parking
  for Distributed parking : a fixed % of the hourly transit flow (1999…. What in 2000?)

## Slide 10: 5. THE KINEMATICS CORRECTION FACTOR (KCF) APPROACH
EMISSIONS ON NETWORK LINKS ARE NORMALLY CALCULATED FROM AVERAGE SPEED, BUT LINKS WITH THE SAME AVERAGE SPEED CAN SHOW VERY DIFFERENT VEHICLE KINEMATICS, AND VERY DIFFERENT EMISSIONS
TO CORRECT THE ‘AVERAGE SPEED EMISSION’ WITH A FACTOR INCLUDING THE EFFECT OF SPEED VARIABILITY ALONG THE LINK CAN REDUCE EMISSION UNCERTAINTY
THE ‘KCF’ CAN BE EXPRESSED AS A FUNCTION OF TRAFFIC DENSITY, GREEN TIME %, LINK LENGTH AND AVERAGE SPEED AND CALCULATED BY THE RECONSTRUCTION OF THE SPEED CYCLE

## Slide 12
FIG. 2 : SPEED CYCLE RECONSTRUCTION : TIME FRACTIONS OF KINEMATIC PHASES VS NORMALISED TRAFFIC DENSITY (QUALITATIVE CURVES)

## Slide 13
FIGURE 3 : TYPICAL RECONSTRUCTED SPEED CYCLES

## Slide 14: 5.1 RESULTS FROM DG XII ESTEEM PROJECT KCF = KCF0 * d(D) * g(G) * l(L) * v(V) for Fuel Consumption (c1 to c14 are optimised coefficients) d(D) = c1 (D < 30) , c2 * D + c3 (30 < D < 90), c4-c5*D ( D>90) g(G) = c6 ,for G < 0.9 , and c7 - c8 * G for 0.9 < G < 1.0 l(L) = c9 + c10 * exp (-L/c11) v(V) = c12 + c13 * exp (-V/c14) for CO emissions d (D) = c1 + c2 * exp (D/c3) (D<90), and d(D) = c4-c5*D (D>90) g(G) = c6 + c7 * exp (-G/c8) l(L) = c9 + c10 * exp (-L/c11) v(V) = c12 - c13 * exp (-V/c14)

## Slide 15
FIG . 4 : KCF for Fuel Consumption full range density profile (10 to 110 vehicles/Km)

## Slide 16
Figure 5 : Measured, calculated (shaded area) and extrapolated CO level at Corso Francia site, for business day