## Slide 1: EMISSION EXPERT PANEL MEETING
Applicazioni del codice TEE 2002
e sviluppi modellistici in corso
E. Negrenti – ENEA
A. Parenti – ASTRAN
P. Aloia - STA
ENEA Sede – 16 Gennaio 2003

## Slide 2: OVERVIEW
1) ELEMENTI INNOVATIVI DEL TEE 2002
2) APPLICAZIONI RECENTI (HEAVEN)
3) SVILUPPI IN AMBITO PROGETTO ISHTAR

## Slide 3: 1.1 ELEMENTI INNOVATIVI DEL CODICE TEE 2002
Modellistica delle emissioni di PM10 (dirette ed indirette) e benzene sviluppata nell’ambito dell’AdP ENEA - MINAMB
Introduzione di nuove categorie veicolari
Introduzione della opzione cinematica “ciclo di guida reale” per il calcolo delle emissioni in una rete stradale descritta con elevato dettaglio sul comportamento dei veicoli (es. output da simulatore)
Implementazione del fattore di correzione cinematica delle ‘hot emissions’ per consumo, CO e COV (funzione di densità lineare, velocità media, lunghezza link e % di verde al semaforo a fine link)

## Slide 4: 1.2 ANDAMENTO DEL ‘KCF’ IN FUNZIONE DEL PARAMETRO DENSITA’ DI TRAFFICO
Fonti delle funzioni di emissione : COPERT (vs vel. media) e MODEM (emissioni istantanee)

## Slide 5: 1.3 LE SORGENTI DI PM10
EMISSIONI DIRETTE
Emissioni allo scarico; dipendono dalla tipologia del veicolo e dal tipo di carburante utilizzato.
EMISSIONI INDIRETTE
Emissioni da usura di freni e pneumatici
Emissioni da degradamento dell’asfalto stradale Emissioni da risospensione dovuta al transito
>>>> Dipendono dalla tipologia di veicolo.

## Slide 6
2.1 Applicazione rete reale
Progetto Europeo: HEAVEN
(Healthier Environment through Abatement of Vehicle Emission and Noise)
Obiettivi: sviluppare un sistema di supporto alle decisioni (DSS) che fornisca informazioni integrate ed in tempo reale sull’inquinamento atmosferico e una visione d’insieme del livello di congestione della rete
Schema attività del progetto HEAVEN
RETE DI
MONITORAGGIO DELLA
QUALITA’ DELL’ARIA
MODELLO EMISSIONI
DA TRAFFICO
VEICOLARE
EMIS
SIONI
MODELLO
DI
DISPERSIONE A SCALA
REGIONALE
MODELLO
DI
DISPERSIONE A SCALA
URBANA
DIFFUSIONE
ACQUISIZIONE DATI
(FLUSSI RILEVATI)
MODELLO DI
ASSEGNAZIONE DEI
FLUSSI DI TRAFFICO
TRAFFICO
OSSERVATORE
(RICOSTRUZIONE STATO
DELLA RETE)

## Slide 7
Traffic Modelling Module
739 oriented links
282 endpoints
51 centroids
Assignment:
TransCAD Transportation GIS Software
Model: Deterministic User Equilibrium
Computational time: 25''
O/D Matrix Correction:
Correction Algorithm developed and implemented by STA
Computational time: 10''
Air Pollution Modelling Module
TEE Model:
Input: road network static data and traffic data
Outputs: emission data (CO, Benzene and NOx) for each link
Computational time: 120''
ADMS Model:
Input: road network static data, emission data and met data
Output: concentrations (CO, Benzene and NOx) on a regular grid
Computational time: 600''



5'
5'
60'
Interfaces With
Existing/External Systems
UTC and TCC Interfaces:
279 measurement stations: flow, speed, queue, occupancy
data acquisition every 5'
METEO Interface:
Integrated interface self-updating with observed data
data acquisition every 60'
Air Quality data Interface:
Integrated interface
data acquisition every day
The On-line HEAVEN system
2.2 Applicazioni del TEE 2002

## Slide 8
2.3 RETE HEAVEN – area di studio
L’area di studio si colloca nell’area centro-nord-est della città di Roma, all’interno dell’Anello Ferroviario
Risulta compresa nella zona interdetta al passaggio delle vetture non catalitiche (1° Gennaio 2002)
La Zona HEAVEN è proporzionalmente rappresentativa dell’intera area urbana della città
Racchiude in sé:
importanti direttrici della viabilità principale (Via Nomentana, Via Salaria, parte del Lungotevere Sinistro)
una buona porzione di viabilità locale
un’ampia zona di verde (Villa Ada, Villa Torlonia)

## Slide 9
Matrice O/D del giorno lavorativo medio
Meteo: T=12° C; velocità vento = 1 m/s e direzione 0°; copertura nuvolosa = 75%
2.4 MAPPA DI CONCENTRAZIONE CO

## Slide 10
2.5 DIFFERENZE TRA CONCENTRAZIONI MISURATE
DALLE CENTRALINE E CONCENTRAZIONI
CALCOLATE DALLA CATENA HEAVEN

## Slide 11: 2.6 COEFFICIENTE DI CORRELAZIONE

## Slide 12: 3. SVILUPPI IN CORSO PER IL CODICE TEE 2003 (Progetto V PQ ISHTAR)
  MODELLING OF VEHICLES KINEMATICS
  MULTIPLE DATABASES USAGE (AVER. SPEED EMISSIONS AND INSTANT. EMISSIONS)
  FLEXIBLE PARKING PROCESS REPRESENTATION FOR IMPROVED COLD EMISSIONS LOCATION
  GENERALISED FLEET COMPOSITION DEFINITION (USER DEFINED VEHICLES)
  MAXIMUM EXTERNALISATION OF FORMULAS
  INSERTION OF ADDITIONAL ALGORHITMS

## Slide 13: 3.1 TEE ROLE IN THE ISHTAR SUITE
TRAFFIC
MODULE
TEE 2003
CONSUMPTION & EMISSION
NOISE
SAFETY
DISPERSION MODULE
OVERALL EVALUATION (CBA, MCA)
EXPOSURE AND HEALTH IMPACT
FLOWS, SPEED
OTHER OUTPUT
POLLUTANTS EM.
NOISE LEVELS,
ACCIDENTS

## Slide 14: DEV1 : MODELLING OF VEHICLES KINEMATICS
Issue : To introduce a corrective factor considering kinematics for reducing the uncertainty connected with the use of average speed based emission functions.
Solution : To extend the methodology developed during the ESTEEM Project (CO, FC) to other pollutants (NOX, VOC) for a set of major vehicle classes (diesel, cat., non cat.) belonging to passenger car.
Needed input from partners : detailed characterisation of the traffic flows hour by hour and of the geometry of the link (number of lanes, semaphore phase at the end of the link, % of green on the total semaphore time.)

## Slide 15: DEV1 - b : TIME FRACTIONS
Issue: to optimise the curves related to the time fractions of the Kinematic phases : march, acceleration, deceleration and stop time fractions. This issue is strategic for the reconstruction of the driving cycles from basic traffic data (flow, density, green % time)
Solution: To extend the matrix of possible realistic driving conditions along the link. To optimise the algorithm, developed during ESTEEM Project, for the cycle reconstruction.
Possible input from partners: driving cycles measured, driving behaviours, Kinematic parameters from measures or traffic micro simulators.

## Slide 16: DEV1) c : RECONSTRUCTED SPEED CYCLES
Examples of different speed cycles reconstructed from different traffic situations

## Slide 17: DEV1 - d : EXPECTED RESULT
Standard formulas of Kinematic corrective factor approach:
Emission = [ Emission (aver. speed) ] * KCF
KCF = KCF(0) *d (D)* l(L)* g(GR%)* v(SPEED)
considered developments in ISHTAR :
Introduction of the relevance on accelerations number and idling time of
  the number of lanes
  Intersections along the link
  Pedestrian crossings (needed also for the safety model)

## Slide 18: DEV2 : MULTIPLE DATABASES USAGE (AVER. SPEED EMISSIONS AND INSTANT. EMISSIONS)
Issue : Insertion of new databases made available in the near future. Fully implement the speed cycle option for the entire city network (e.g. this option can be used when input is from SATURN)
Solution : linkage with Projects producing new data (Artemis, COST346). Introduction of a set of libraries containing the standard European speed cycles.
Input from partners : access to results from involved projects. Detailed speed cycles data provided by the traffic models like SATURN

## Slide 19: DEV3 : PARKING MODEL FOR IMPROVED COLD EMISSIONS LOCATION
Issue : to introduce the consideration of parking and inserting flows of vehicles link by link.
Method : to estimate parking flows and parking speed cycles in order to optimise the data present in the TEE code.
Input from partners (cities):
  a) information on the concentrated parking (existence and capacity) and of distributed parking along the link.
  b) position of the inlet and outlet of the Parking along the links interested by the concentrated parking areas
  c) characterisation of the type of parking (for passenger cars, heavy vehicles, buses, motorcycles)
  d) curves of parking occupancy rate (e.g. by hour, by day category, by area category)

## Slide 20: DEV4 :GENERALISED FLEET COMPOSITION DEFINITION (USER DEFINED VEHICLES)
Issue : to generalise the definition of the urban scale and link based fleets also allowing the user definition of new vehicles.
Solution: to implement the best way to insert all the parameters and coefficients characterising the emission and consumption functions related to the new and future (and old….) vehicle categories.
Input from partners : definition of expectations (what might be the new vehicles representation needs ?…..)

## Slide 21: DEV5 : MAXIMUM ‘EXTERNALISATION’ OF FORMULAS
Issue : to allow the future user to input ‘model-data’ (e.g. emission functions of new and old vehicles, or sensitivity factors to the affecting parameters).
Method : to identify general formulas for emission functions or use external abacus (also in order to simplify the insertion of new vehicle emission and consumption functions - see fleet generalisation issue)
Input from partners : feedback on the more user friendly solutions and comments in order to implement new user oriented approaches for the data insertions.

## Slide 22: DEV6 : INSERTION OF ALGHORITMS
Introduction of load correction for HDV.
Complete revision of cold emission model (the cities must provide cold % info from traffic models output (average driven length per link)).
Extension link by link of MEET approach for evaporative emissions. Definition of vehicles with injection or canister system (COPERT III or COMMUTE evap. Model).
Introduction of energy fuel life cycle and vehicle life cycle (only at aggregated level).
Introduction of air conditioning effect.
Introduce overall checks of consistency

## Slide 23: DEV7 and DEV8 : INTEGRATION OF NOISE and SAFETY MODELS
Introduction of the simplified two - dimensional noise model in alternative to the detailed 3D model (WP4 issue). This simplified model will be used for the analysis of large city projects/measures (such as the Rome or Paris or Athens case studies) for which the availability of detailed input data is unlikely, the running-time of a detailed analysis would be too high, and the significance of a sophisticated approach is lower.
Input needed by the ISHTAR cities: Link-buildings characteristics ( average height of buildings along the link).
Introduction of the safety model (by Lassarre).
Input needed by ISHTAR cities: Pedestrian movements, crossing information

## Slide 24: DEV 9 : extend 24hr capability
Issue : to allow 24 hr calculation of emissions, noise and accidents on the basis of a common traffic information (received by WP2 tools and-or post processed within Trafic subroutine of TEE)
Input from partners :
  Flow profiles on selected types of links along the 24hrs
    Data on parking process (occupancy, flows)

## Slide 25: TEE 2003 : ACTIONS COMPLETED
Introduction of micro – macro category relationship.
Development of daily traffic curves depending by day and area category. (Input needed by ISHTAR cities for the curves calibration).
Introduction of a complete set of vehicular categories (see COPERT III characterisation) also for future fleet development with their c. & e. functions.
Introduction of macro fleet composition to be inserted in alternative to the micro fleet distribution.
Checking the temporal and spatial loops
Introduction of micro and macro checks on the calculation flow and input data congruity.
Introduction of the emission calculation related to Benzene (as % of VOC) and PM10 (as % of PTS)